## Slide 1: RTC (REAL TIME CLOCK)IN LPC2148

## Slide 2: Introduction to RTC
Measures the passage of time to maintain a calendar and clock using counters when the system is ON and optionally when it is OFF.
Ultra Low Power design to support battery powered systems (3.3 V).
Provides Seconds, Minutes, Hours, Day of Month, Month, Year, Day of Week, and Day of Year.
Programmable Reference Clock Divider allows adjustment of the RTC to match various crystal frequencies.

## Slide 3: Block diagram of RTC

## Slide 4: Register Description
Registers are split into four sections by their functionality…
i. Miscellaneous Register Group (8-reg).
ii. Time Counter Group (8-reg).
iii. Alarm Register Group (8-reg).
iv. Prescalar register(2-reg).

## Slide 5: Miscellaneous Register Group
ILR (Interrupt Location Register)
CTC (Clock Tick Counter)
CCR (Clock Control Register)
CIIR (Clock Increment Interrupt Register)
AMR (Alarm Mask Register)
CTIME0 (Consolidated Time Register 0)
CTIME1 (Consolidated Time Register 1)
CTIME2 (Consolidated Time Register 2)

## Slide 6: Interrupt Location Register (ILR)
This Register specifies which block is generating interrupt and writing 1 will clear the interrupt.
7 6 5 4 3 2 1 0
RTCALF : Clears the interrupt generated by Alarm
RTCCIF : Clears the interrupt generated by Counter Increment Interrupt
 |  |  |  |  |  | RTCALF | RTCCIF

## Slide 7: Clock Tick Counter (CTC)
Clock Tick Counter :
This register act as counter register, this register counts 32,768 clocks per second (This is variable based on the prescaler value).

## Slide 8: Clock Control Register (CCR)
These registers controls the RTC
7 6 5 4 3 2 1 0
CLKEN: Writing logical One will enable the clock for RTC. And Zero on this bit will disable RTC.
CTCRST: Writing logical one on this bit will clear CTC register. CTC will clear till this bit is one.
CTTEST: This bit enables test. These bits must be zero during normal operation.
CLKSRC: When this bit is one it takes external oscillator as clock source and zero means it takes the internal clock source.
 |  |  |  | CLKSRC | CTTEST | CTCRST | CLKEN

## Slide 9: Counter Increment Interrupt Register (CIIR)
This register enables interrupt when a counter is incremented and this interrupt can be cleared by writing logical 1 to ILR 0th bit (RTCCIF).
7 6 5 4 3 2 1 0
BIT 0: IMSEC: Logical one on this bit will generate interrupt for increment in second value.
BIT 1: IMMIN: Logical one on this bit will generate interrupt for increment in Minute value.
IMYEAR | IMMON | IMDOY | IMDOW | IMDOM | IMHOUR | IMMIN | IMSEC

## Slide 10: CONTND…..
BIT 2: IMHOUR: Logical one on this bit will generate interrupt for increment in hour value
BIT 3: IMDOM: Logical one on this bit will generate interrupt for increment in day of month value
BIT4: IMDOW: Logical one on this bit will generate interrupt for increment in day of week value
BIT5: IMDOY: Logical one on this bit will generate interrupt for increment in s day of year value
BIT 6: IMMON: Logical one on this bit will generate interrupt for increment in month value
BIT 7: IMYEAR: Logical one on this bit will generate interrupt for increment in year value

## Slide 11: Alarm Mask Register (AMR)
This register is used to enable/disable corresponding interrupt generate because of the value present in the Alarms registers.
7 6 5 4 3 2 1 0
BIT0: AMRSEC: When this bit is written one, the second value will not compared for alarm.
BIT1: AMRMIN: When this bit is written one, the minute value will not compared for alarm.
BIT2: AMRHOUR: When this bit is written one, the hour value will not compared for alarm.
AMR YEAR | AMR MON | AMR DOY | AMR DOW | AMR DOM | AMR HOUR | AMR MIN | AMRSEC

## Slide 12: CNTND…..
BIT3: AMRDOM: When this bit is written one, the day of month value will not compared for alarm
BIT4: AMRDOW: When this bit is written one, the day of the week value will not compared for alarm
BIT5:AMRDOY: When this bit is written one, the day of the year value will not compared for alarm
BIT6:AMRMON: When this bit is written one, the month value will not compared for alarm
BIT7:AMRYEAR: When this bit is written one, the year value will not compared for alarm

## Slide 13: Alarm Register group
Name of the
register Size Description
ALSEC 6 Contains alarm value of second
ALMIN 6 Contains alarm value of minute
ALHOUR 5 Contains alarm value of hour
ALDOM 5 Contains alarm value of day of the month
ALDOW 3 Contains alarm value of day of the week
ALDOY 9 Contains alarm value of day of the year
ALMONTH 4 Contains alarm value of the month
ALYEAR 12 Contains alarm value of the year

## Slide 14: Time Counter Register Group
Name of
the register Size Description
SEC 6 Contains value of second
MIN 6 Contains value of minute
HOUR 5 Contains value of hour
DOM 5 Contains value of day of the month
DOW 3 Contains value of day of the week
DOY 9 Contains value of day of the year
MONTH 4 Contains value of the month
YEAR 12 Contains value of the year

## Slide 15: Reference Clock Divider
The reference clock divider (hereafter referred to as the Prescaler) allows generation of a 32.768 kHz reference clock from any peripheral clock frequency greater than or equal to 65.536 kHz (2 x 32.768 kHz).
This permits the RTC to always run at the proper rate regardless of the peripheral clock rate.
Prescaler divides the peripheral clock (pclk) by a value which contains both an integer portion and a fractional portion. The result is not a continuous output at a constant frequency, some clock periods will be one pclk longer than others. However, the overall result can always be 32,768 counts per second.

## Slide 16: Prescalar Integer registers
PREINT (13-bit reg)
This is the integer portion of the prescale value, calculated as:
PREINT = int (pclk / 32768) - 1.
The value of PREINT must be greater than or equal to 1.
PREFRAC (15-bit reg)
This is the fractional portion of the prescale value, and may be calculated as:
PREFRAC = pclk - ((PREINT +1) x 32768).

## Slide 17: Example
In a simplistic case, the pclk frequency is 65.537 kHz. So:
PREINT = int (pclk / 32768) - 1 = 1 and
PREFRAC = pclk - ((PREINT +1) x 32768) = 1
With this prescaler setting, exactly 32,768 clocks per second will be provided to the RTC by counting 2 pclks 32,767 times, and 3 pclks once.
In a more realistic case, the pclk frequency is 10 MHz. Then,
PREINT = int (pclk / 32768) - 1 = 304 and
PREFRAC = pclk - ((PREINT +1) x 32768) = 5,760.
In this case, 5,760 of the prescaler output clocks will be 306 (305+1) pclks long, the rest will be 305 pclks long.

## Slide 18: RTC INTERFACING
Select the port.
Enable reg select.
Enable clock(clk division).
Load values in sec, min, hour, DOM, month, and year.
Convert values into bcd.
Send to lcd.

## Slide 19
SEC(6) : sec’s reg ( 0 to 59)
MIN(6) : min’s reg ( 0 to 59)
HOUR(5) : hr’s reg ( 0 to 23)
DOM(5) : day of month reg ( 1 to 28,29, 30 or 31 depending on month and whether leap year)
MONTH(4) : month’s reg ( 1 to 12)
YEAR(12) : year’s reg (0 to 4095)

## Slide 20: REF CLK DIVIDER(PRESCALAR)
Prescalar int reg:
PREINT(13) = 0 x 0000 0392 or 0X5A(with pclk=3Mhz)
=int(pclk/32768) – 1
Its value >=1
15-13 bit : reserved (XXX)
12:0 bit : Prescalar int RTC prescalar value
160 MHz/32,768 – 1 = 4881( 13 bits to hold) and remainder( val could be as large as 32,767 which requires 15 bits) 26, 624

## Slide 21
Prescalar frac reg :
PREFRAC(15) = 0 x 0000 4389 or 0X46C0(3Mhaz)
15 bit : reserver(X)
14 – 0 bit : frac portion of RTC prescalar value.
PREFRAC = pclk – ((PREINT +1)X 32768)
PINSEL0 = 0X 0005 0000; or PINSEL0=0X0000005; select TXD0 and RXD0 lines
VPBDIV = 0X 02; // PREINT = int(pclk/32768)-1

## Slide 22: REFERENCES
UM10139 Volume 1: LPC214x User Manual Rev. 02 — 25 July 2006 User manual LPC214x

## Slide 23: REFERENCES
UM10139 Volume 1: LPC214x User Manual Rev. 02 — 25 July 2006 User manual LPC214x

## Slide 24
THANK YOU